## Slide 1
PHY 712 Electrodynamics
10-10:50 AM in Olin 103
Notes for Lecture 21:
    Chap. 8 (Sec. 8.1-8.4 in JDJ)
    Wave Guides (shortened lecture)
      TEM, TE, and TM modes
      Justification for boundary conditions; behavior of waves near conducting surfaces

## Slide 2
For 3/04/2024-3/08/2024:
  Individual work on take home exam
  Shortened class lectures on Chapter 8 of Jackson

## Slide 3
Maxwell’s equations

## Slide 4
Analysis of Maxwell’s equations without sources -- continued:

## Slide 5
Analysis of Maxwell’s equations without sources -- continued:
Both E and B fields are solutions to a wave equation:

## Slide 6
Analysis of Maxwell’s equations without sources -- continued:
Note: e, m, n, k can all be complex; for the moment we will assume that they are all real (no dissipation).
For real
e, m, n, k

## Slide 7
Analysis of Maxwell’s equations without sources -- continued:
E0
B0
k

## Slide 8
Transverse electric and magnetic waves (TEM)
E0
B0
k
TEM modes describe electromagnetic waves in lossless media and vacuum
For real
e, m, n, k

## Slide 9
Effects of complex dielectric; fields near the surface on an ideal conductor

## Slide 10
Some details:

## Slide 11
Fields near the surface on an ideal conductor -- continued
“skin depth”

## Slide 12
Some representative values of skin depth
Ref: Lorrain2 and Corson
 | s (107 S/m) | m/m0 | d (0.001m) at 60 Hz | d (0.001m) at 1 MHz
Al | 3.54 | 1 | 10.9 | 84.6
Cu | 5.80 | 1 | 8.5 | 66.1
Fe | 1.00 | 100 | 1.0 | 10.0
Mumetal | 0.16 | 2000 | 0.4 | 3.0
Zn | 1.86 | 1 | 15.1 | 117

## Slide 13
Relative energies associated with field

## Slide 14
Fields near the surface on an ideal conductor -- continued
z
r||
0

## Slide 15
Fields near the surface on an ideal conductor -- continued
z
r||
0

## Slide 16
Boundary values for ideal conductor
At the boundary of an ideal conductor, the E and H fields decay in the direction normal to the interface.
H0
E0

## Slide 17
Waveguide terminology
  TEM: transverse electric and magnetic (both E and H fields are perpendicular to wave propagation direction)
  TM: transverse magnetic (H field is perpendicular to wave propagation direction)
  TE: transverse electric (E field is perpendicular to wave propagation direction)
Wave guides – dielectric media with one or more metal boundary
E
H
Continuity conditions for fields near metal boundaries --

## Slide 18
Analysis of rectangular waveguide
Boundary conditions at surface of waveguide:
Etangential=0, Bnormal=0
z
x
y
Cross section view
b
a

## Slide 19
Analysis of rectangular waveguide
z
x
y

## Slide 20
Solution of Maxwell’s equations within the pipe:
F = E or H
propagation along z.

## Slide 21
Maxwell’s equations within the pipe in terms of all 6 components:

## Slide 22
TE modes for rectangular wave guide continued:

## Slide 23
Solution for m=n=1

## Slide 24
Solution for m=n=1
k
w

## Slide 25
Solution for m=n=1 -- more details
(direction along the wave guide)