# Problems for February 23, 2000

Problem 2.  Microwaves in a microwave oven are produced by electrons circling in a magnetic field at a frequency of 2.4 GHz.

- What is the magnetic field strength?

- The electrons’ motion takes place inside a special tube called a magnetron.  If the magnetron can accommodate electron orbits with a maximum diameter of 2.5 mm, what is the maximum electron energy?

Problem 3.  An electron moves in a circular path perpendicular to a constant magnetic field of magnitude 1.00 mT.  If the angular momentum of the electron about the center of the circle is 4.00(10-25 J(s, determine

- the radius of the path, and

- the speed of the electron.

Problem 4. A cyclotron designed to accelerate protons has a magnetic field of magnitude 0.45 T over a region of radius 1.2 m.  What are

- the cyclotron frequency, and

- the maximum speed acquired by the protons?

Problem 5.  A cyclotron is designed to accelerate deuterium nuclei.  (Deuterium has one proton and one neutron in its nucleus.)

- If the cyclotron uses a 2.0 T magnetic field, at what frequency should the dee voltage be alternated?

- If the vacuum chamber has a diameter of 0.90 m, what is the maximum kinetic energy of the deuterons?

- If the magnitude of the potential difference between the dees is 1500 V, how many orbits do the deuterons complete before achieving the energy of part (b)?

Here's a picture of the cyclotron.  You can also refer to the Encyclopedia Britannica reference in the reading assignment for Feb. 18.