Note: The methyl groups shown (incorrectly) in the product should be H’s.

Plan to use the modified procedure on the next page.

Plan to use this…

Modified Diels-Alder Procedure

Using a powder funnel, add 3-sulfolene (4.25 g) and powdered maleic anhydride (2.25 g) into a dry, 50 mL round bottom flask.  Add 4 mL xylene, fit the flask with a condenser, and add a plug of cotton to the top of the condenser (Note 1).  Gently swirl flask to effect partial solution.  Remove cotton plug and cautiously heat the mixture to a slow boil (Notes 2 and 3).  Boil the mixture for 45 minutes, adding more heat during the last 15 minutes to maintain a steady reflux.  Allow the flask to cool for 1-2 minutes (*Note 4*) and then add 20 mL toluene (Note 5).  Heat the toluene solution as necessary to dissolve any solids.  Transfer to a 125 mL Erlenmeyer flask.  Add heptane until a slight cloudiness persists.  (You want a hot, saturated solution for a duel-solvent crystallization.)  Allow the solution to cool to room temperature and then in an ice bath.  Isolate the product by vacuum filtration.

Obtain a weight and melting point for the dry product.